PowerPoint-Präsentation
Device-mapper RAID tool
(dmraid)
Linux-Kongress Hamburg 2005
Heinz Mauelshagen
Consulting Development Engineer
Linux-Kongress 2005

---
device-mapper Raid Tool
Top
ATARAID
requirements
device-mapper architecture/features
dmraid architecture/features
user Interface
usage examples
project Status/Summary
URLs

---
ATARAID
ATARAID is a generic term for a variety of cheap vendor
 software RAID solutions (eg, Highpoint, Silicon Image, ...)
typically combines a number of P/SATA adaptors
 (HBA and/or on MoBo), a BIOS extension, a host OS driver
 and a management tool
BIOS extension supports creation of vendor specific
 metadata describing RAID devices/sets through
 a UI and mapping created RAID sets as a single device
OS driver contains the actual RAID logic (ie. mirroring);
 Windows version shipped with the product
RAID driver for a subset of solutions were part of Linux 2.4
Device-mapper in Linux 2.6 avoids having seperate
 RAID drivers for each solution

---
Requirements
Device-Mapper runtime
Tool to:
discover ATARAID devices
retrieve RAID properties from vendor metadata
group RAID sets
create/remove mapped devices (ie. logical devices)
display RAID device/set properties
handle device events (eg, disk failure)
avoid hardware dependencies by ignoring interface
 types completely

---
Software-Architecture (1)
Device-Mapper is the generic mapping runtime platform in
 the Linux kernel (since 2.5)
can be used by multiple applications which need
 block device mapping (eg, dmraid, LVM2 or EVMS)
manages Mapped-Devices (create, remove, …)
handles text formatted Mapping-Tables (load, unload, reload)
all table loading actions happen online to reflect changed
 layouts (eg, a MD size change)
code to handle mappings factored out into Mapping-Targets,
 which handle linear, striped, mirrored, snapshot, multipath,
 zero, error and crypt layouts
maps to arbitrary block devices (eg, (i)SCSI)

---
Software-Architecture (2)
Device-Mapper (continued...)
Mapping-Targets are dynamically loadable and register with
 the Device-Mapper core
Mapped-Devices can be stacked in order to build complex
 mappings (eg, to create a RAID10 set)
more than 2 Terabytes per mapped device in Linux 2.6
 (CONFIG_LBD)
comes with a user space library to be interfaced by
 Device/Volume Management applications and a test
 tool dmsetup
lib creates nodes to access Mapped Devices in /dev/mapper/

---
Software-Architecture (3)
Examples of Device-Mapper tables which can be activated
 using the dmsetup tool
0 1024 linear /dev/hde1 40
 1024 2048 striped 2 64 /dev/hde1 1064 /dev/hdf1 0
0 1024 zero
 1024 1000 error
0 83886080 mirror core 1 64 2 /dev/sda 0 /dev/sdb 0

---
Software-Architecture (4)
dmraid application falls appart into tool and library
dmraid library functional areas:
discovery of block devices
retrieval of device properties (ie. path, size, serial#)
multi RAID metadata format registry (format handlers)
discovery of RAID devices (ie. metadata)
translation of particular metadata format
 into internal generic RAID device representaion
grouping of RAID sets (hierarchical with eg. RAID10)
 represented via internal generic format
derivation of mapping tables from internal
 RAID device/set format

---
Software-Architecture (5)
library functional areas (continued...):
creation of mapped devices
activation of (stacked) mappings
logging of block/RAID device and RAID set properties

---
Software-Architecture (6)
tool functional areas (continued...):
display discovered block devices
display discovered RAID devices
display grouped RAID sets
(de)activate RAID sets
dump/erase native ATARAID metadata
list supported metadata formats
help

---
Architecture Overview
Userspace
Kernelpace
dm = device-mapper core
lld = low level driver
tool
libdmraid
dm
libdm
target
target
target
lld

---
User Interface (1)
'dmraid' tool
-b : display discovered block devices
-l : list all supported metadata formats
-r : display discovered RAID devices
-s : display grouped RAID sets
-n : display native metadata
-ay : activate all grouped RAID sets
-an : deactivate all grouped RAID sets
-tay : display mapping tables

---
User Interface (2)
'dmraid' tool
-rD : dump vendor metadata into files
-rE : erase vendor metadata on devices
-h : help
-r, -s and -a optionally take -f to select formats
 (identifiers as listed with -l; eg, '-fhpt,sil')
-r and -n take an optional list of device paths
-ay, -an and -s take an optional list of RAID set names

---
Examples (1)
# dmraid -l
hpt37x : Highpoint HPT37X (S,0,1,10,01)
hpt45x : Highpoint HPT45X (S,0,1)
isw : Intel Software RAID (0,1)
lsi : LSI Logic MegaRAID (0,1,10)
nvidia : NVidia RAID (S,0,1,10)
pdc : Promise FastTrack (S,0,1)
sil : Silicon Image(tm) Medley(tm) (0,1,10)
via : VIA Software RAID (S,0,1,10)
dos : DOS partitions on SW RAIDs

---
Examples (2)
# dmraid -b
/dev/sda: 72170879 total, "680631431K"
/dev/sdb: 8887200 total, "LG142316"
/dev/sdc: 72170879 total, "680620811K"
/dev/dm-14: 312581808 total, "N/A"
/dev/dm-18: 312581808 total, "N/A"
/dev/dm-22: 234441648 total, "N/A"
/dev/dm-26: 234441648 total, "N/A"
/dev/dm-30: 312581808 total, "N/A"
/dev/dm-34: 312581808 total, "N/A"

---
Examples (3)
# dmraid -r
/dev/dm-30: sil, "sil_afadbgdebbde", stripe, ok, 312578720 sectors, data@ 0
/dev/dm-34: sil, "sil_afadbgdebbde", stripe, ok, 312578720 sectors, data@ 0
/dev/dm-14: hpt37x, "hpt37x_badgbjbbhb-3", stripe, ok, 78165248 sectors, data@ 0
/dev/dm-18: hpt37x, "hpt37x_badgbjbbhb-3", stripe, ok, 78165238 sectors, data@ 10
/dev/dm-22: hpt37x, "hpt37x_badgbjbbhb-2", stripe, ok, 78165248 sectors, data@ 0
/dev/dm-26: hpt37x, "hpt37x_badgbjbbhb-2", stripe, ok, 78165238 sectors, data@ 10
# dmraid -r /dev/dm-34
/dev/dm-34: sil, "sil_afadbgdebbde", stripe, ok, 312578720 sectors, data@ 0

---
Examples (4)
# dmraid -s hpt37x_badgbjbbhb
*** Superset
name : hpt37x_badgbjbbhb
size : 156330476
stride : 128
type : raid10
status : ok
subsets: 2
devs : 4
spares : 0
# dmraid -cc -s
hpt37x_badgbjbbhb:156330476:128:raid10:ok:2:4:0
sil_afadbgdebbde:625157440:32:stripe:ok:0:2:0

---
Examples (5)
# dmraid -tay
sil_afadbgdebbde: 0 625157440 striped 2 32 /dev/dm-30 0 /dev/dm-34 0
hpt37x_badgbjbbhb-2: 0 156330476 striped 2 128 /dev/dm-22 0 /dev/dm-26 10
hpt37x_badgbjbbhb-3: 0 156330476 striped 2 128 /dev/dm-14 0 /dev/dm-18 10
hpt37x_badgbjbbhb: 0 156330476 mirror core 2 64 nosync 2 \
/dev/mapper/hpt37x_badgbjbbhb-2 0 /dev/mapper/hpt37x_badgbjbbhb-3 0

---
Status and Future Directions
Device-Mapper in Linux 2.6 Mainline
 -> Distributors are shipping it
dmraid shipped with Debian, Fedora, RHEL, SuSE, ...
anaconda support for dmraid in the works
use dmeventd for device monitoring
support SNIA DDF
support RAID levels > 1

---
Summary
dmraid utilizes the generic mapping capabilties of
 device-mapper in order to make a growing number
 of ATARAID solutions available on Linux 2.6

---
URLs
http://sources.redhat.com/dm (Device-Mapper tool+library)
http://people.redhat.com/heinzm/sw/dmraid/
http://www.redhat.com/mailman/listinfo/ataraid-list
 to subscribe to ataraid-list@redhat.com

---
Q & A